## Emergency Action Plan (EAP)

## Rock Creek Watershed, Dam No. 23

## (Rock City Lake)

### National Inventory of Dams (NID) No. OK11111

### Section 14, T13N, R21

### Latitude: 35.42875; Longitude: -99.19802

#### Coal County, Oklahoma

Coal County Conservation District

With assistance from the 
U.S. Department of Agriculture
Natural Resources Conservation Service

Emergency Action Plan Prepared By:

_________________________________

Jane Smith, Dam Owner

_______________________

Date

Copy        of  ___

Contents

Basic EAP Data	3

EAP Overview	4

Roles and Responsibilities	5

The Five-step EAP Process

Step 1	Event Detection 	7

Step 2	Emergency Level Determination	7

Guidance for Determining the Emergency Level 	9

Examples of Emergency Situations	10

Step 3	Notification and Communication	12

Notification Charts	14

Other Emergency Services Contacts	17

Step 4	Expected Actions	18

Step 5	Termination and Follow up	21

Maintenance—EAP Review and Revision	22

Record of Holders of Control Copies of this EAP	24

Record of Revisions and Updates Made to EAP	25

Appendices—Forms, Glossary, Maps, and Supporting Data	26

Appendix A

Appendix A–1 	Unusual or Emergency Event Log Form	27

Appendix A–2 	Dam Emergency Situation Report Form	28

Appendix A–3 	Glossary of Terms	29

Appendix A-4 		Contact Checklist………………………………………………………………32

Appendix B

Appendix B–1 	Resources Available	33

Appendix B–2 	Location and Vicinity Maps	33

Appendix B–3	Watershed Project Map	34

Appendix B–4 	Inundation Maps	35

Appendix B–5	Residents/Businesses/Highways at Risk	37

Appendix B–6		Residents/Businesses/Highways at Risk with High Auxiliary Spillway Flow	38

Appendix B–7 	Plan View of Dam	39

Appendix B–8 	Profile of Principal Spillway	40

Appendix B–9 	Reservoir Elevation-Area-Volume and Spillway Capacity Data	41

Appendix B–10 	National Inventory of Dams (NID) Data	42

Basic EAP Data

##### Purpose

The purpose of this EAP is to reduce the risk of human life loss and injury and minimize property damage during an unusual or emergency event at Rock Creek Watershed, Dam No. 23 in county and State. It defines responsibilities and procedures to identify conditions that might endanger the dam, notify appropriate emergency personnel, and take possible mitigating actions.

##### Potential Impacted Area

See Inundation Map tab (appendix B–4) and People at Risk tab (appendix B–5) for the locations and contact information of the following residents and businesses that may be flooded if the dam should fail and, if available, the estimated time for the flood wave to travel from the dam to these locations:

(Describe homes, businesses, and roads in downstream evacuaion area)

##### Dam Description

Height:        ft.	Drainage Area:       square miles
Built:       	Hazard Potential Classification: High
Legal Description: Sects. 14 and 23, T13N, R21W	Dam Owner: Coal County Conservation District
Latitude:         Longitude:      	Major Property Owner:      
National Inventory of Dams No.:      	Dam Designer: NRCS

See detailed design data in Appendix B tab.

Directions to dam (See Location and Vicinity Maps; appendix B-2 and B-3)

Rock Creek Watershed, Dam No. 23, can be accessed by traveling south 1.2 miles on OK Highway 44 from the Interstate 40 interchange south of Rock City; turn right (west) on a gated dirt road that goes directly to the left abutment of the dam. Keys for the lock on the gate are available from the Conservation District Manager at 523 Second Street, Rock City, OK. Note that a portion of this road is within the dam breach inundation area, and the valley below the dam may be flooded.

##### An alternate route to the dam is available approximately 0.5 miles south of Rock Creek on Highway 44; turn right on an ungated dirt road that goes to the right abutment of the dam. Note that Highway 44 may be inundated or the bridge may be damaged, so access to this alternate route may have to be gained from Highway 44 south of the dam.

Roles and Responsibilities

##### Dam Owner’s Representative (Conservation District Manager)

- As soon as an emergency event is observed or reported, immediately determine the emergency level

See Emergency Levels tab.

–  High Flow Emergency Level: flooding of downstream people or infrastructure possible

–	Nonfailure Emergency Level: unusual event, slowly developing

–	Potential Failure Emergency Level: potential dam failure situation, rapidly developing

–	Imminent Failure Emergency Level: dam failure appears imminent or is in progress

##### •	Immediately notify the personnel in the order shown on the notification chart for the appropriate level (see Notification Charts tab).

##### •	Provide updates of the situation to the incident commander to assist them in making timely and    accurate decisions regarding warnings and evacuations.

##### Keep in contact with incident commander, public information officer, technical representatives, and State dam safety agency to communicate current conditions. Take corrective actions and respond to emergencies throughout the event.

• Ensure that the EAP and other critical documents are current in DamWatch.

- Monitor DamWatch alerts and prepare tickets to document actions taken.

- Provide leadership to ensure the EAP is reviewed and updated annually and copies of the revised EAP are distributed to all who received control copies of the original EAP.

##### Incident Commander (county sheriff)

•	Serve as the person responsible for coordination of all downstream emergency actions.

•	When a High Flow or Potential Failure Level situation occurs: Prepare emergency management personnel and the downstream population at risk for possible evacuations that may be needed.

•	When an Imminent Failure Level situation occurs:

–	Initiate warnings and order evacuation of people at risk downstream of the dam.

–	Notify local emergency management services to carry out the evacuation of people and close roads within the inundation area (see Inundation Map tab)

• Employ measures to control access to the site and potential downstream hazards.

•	Decide when to terminate the emergency in consultation with qualified dam engineering personnel from the State dam safety agency.

•	Participate in an annual review and update of the EAP.

Kansas Dam Safety Representatives

• Serve as the primary contact person responsible for coordination of all emergency actions regarding the dam.

•Advise the dam operator of the emergency level determination, if time permits.

•	Advise the dam operator of remedial actions to take if Potential Failure Level event occurs, if time permits.

• All media contact and communication will need to go through the Dam Safety representative.

• Provide identification measures for all personnel onsite.

• Participate in an annual review and update of the EAP.

##### Emergency Management Services (Rock City)

- Prepare evacuation plans and procedures prior to the incident.

•	When a High Flow or Potential Failure Level situation occurs:

–	Prepare emergency management personnel for possible evacuations that may be needed if an Imminent Failure Level situation occurs.

–	Alert the public as appropriate.

•	When a High Flow or Imminent Failure Level situation occurs:

–	Alert the public.

–	Immediately close roads and evacuate people in the evacuation area (see Inundation Map tab).

•	Participate in an annual review and update of the EAP.

##### Dam Operator’s Technical Representatives (NRCS)

•	Advise the dam operator of the emergency level determination, if time permits.

•	Advise the dam operator of remedial actions to take if Potential Failure Level event occurs, if time permits.

- Participate in an annual review and update of the EAP.

## The Five-Step EAP Process

Step 1	Event Detection

This step describes the detection of an unusual or emergency event and provides information to assist the dam operator in determining the appropriate emergency level for the event. Early detection of unusual events and evaluation of the condition of the dam is crucial.

Detect unusual or emergency events by—

•	A DamWatch rainfall alert, spillway flow alert, or seismic alert.

- Observations at or near the dam by landowners, government personnel (local, State, or Federal), visitors to the dam, or the public.

•	Evaluation of instrumentation data.

•	Earthquakes felt or reported in the vicinity of the dam.

•	Forewarning of conditions that may cause an unusual event or emergency event at the dam, such as a DamWatch forecast alert or a severe weather or flash flood forecast).

See Guidance for Determining the Emergency Level table on page 8 for assistance in evaluating specific events to determine if they are unusual or potential emergency situations.

Step 2	Emergency Level Determination

After an unusual or emergency event is detected or reported, the conservation district manager  or his or her alternate is responsible for classifying the event into one of the following four emergency levels:

High Flow Emergency Level—No dam failure expected, but flooding of downstream people or infrastructure possible:

This situation indicates that the spillway or low-level outlet works is operating as intended with a large discharge that may cause flooding of downstream roads, homes, businesses, or other infrastructure, but there is no apparent threat to the integrity of the dam. The county sheriff should be informed if it is determined that the auxiliary flow depth is approaching a predetermined safe channel discharge capacity that could threaten downstream areas so that appropriate warnings, road closures, or evacuation actions can be taken. For dams that have no downstream impacts from the spillway or outlet works releases, this emergency level will not be necessary.

Nonfailure Emergency Level—Nonemergency, unusual event, slowly developing:

This situation is not normal, and although it has not yet threatened the operation or structural integrity of the dam, it could if it continues to develop. Contact NRCS technical representatives and State dam safety officials to investigate the situation and recommend actions to take. Closely monitor the condition of the dam monitored, especially during storm events, to detect any development of a potential or imminent dam failure situation. Inform the county sheriff when it is determined that the conditions may quickly develop into a worse condition that may require emergency actions.

Potential Failure Emergency Level—Potential dam failure situation, rapidly developing:

This situation may eventually lead to dam failure and flash flooding downstream, but there is not an immediate threat of dam failure. The county sheriff should be notified of this emergency situation and be advised to “prepare to evacuate.”  This would include issuing a dam failure watch to the population at-risk downstream. The dam operator should closely monitor the condition of the dam and periodically report the status of the situation to the sheriff. If the dam condition worsens and failure becomes imminent, immediately notify the county sheriff of the change in the emergency level and the need to evacuate the people at risk downstream.

If time allows, contact NRCS and State dam safety officials to evaluate the situation and recommend remedial actions to prevent failure of the dam. The dam operator should start remedial repairs (note local resources that may be available—see appendix B–1). Time available to employ remedial actions may be hours or days.

Imminent Failure Emergency Level—Urgent; dam failure is imminent or is in progress:

This is an extremely urgent situation when a dam has failed, is failing, or is about to fail. Flash flooding will occur downstream of the dam. This situation is also applicable when flow through the earth spillway is causing downstream flooding of people and roads. Immediately contact the county sheriff and advise of the necessity to immediately begin evacuations of all at-risk people and close roads as needed (see Inundation Map tab).

See the following pages for guidance in determining the proper emergency level for various situations.

## Guidance for Determining the Emergency Level

| Event | Situation | Emergency level* |
| --- | --- | --- |
| Spillway flow | DamWatch spillway flow alert received | Nonfailure |
|  | Reservoir water surface elevation at auxiliary spillway crest or spillway is flowing with no active erosion | Nonfailure |
|  | Earth spillway flowing with active gully erosion | Potential |
|  | Spillway flow that could result in flooding of people downstream if the reservoir level continues to rise | Potential |
|  | Earth spillway flowing with an advancing head cut that is threatening the control section | Imminent |
|  | Dam discharges are approaching the safe channel capacity shown in appendix 6 that will threaten downstream people or infrastructure | High Flow |
| Embankment overtopping | Reservoir level is less than 1 foot below the top of the dam or water is flowing over the top of the dam with no erosion occurring | Potential |
|  | Water from the reservoir is flowing over the top of the dam with erosion observed | Imminent |
| Seepage | New seepage areas in or near the dam | Nonfailure |
|  | Seepage areas with cloudy discharge or increasing flow rate | Potential |
| Sinkholes | Observation of a vortex in the reservoir or near the embankment | Potential |
|  | Rapidly enlarging sinkhole | Imminent |
| Embankment cracking | New cracks in the embankment greater than ½-inch wide without seepage | Nonfailure |
|  | Cracks in the embankment with seepage | Potential |
| Embankment movement | Visual movement or slippage of the embankment slope | Nonfailure |
|  | Sudden or rapidly moving slides of the embankment slopes | Imminent |
| Instruments | Abnormal instrumentation readings beyond predetermined values | Nonfailure |
| Earthquake | DamWatch seismic alert received or 4.0-magnitude or greater earthquake reported within 25 miles of the dam | Nonfailure |
|  | Earthquake resulting in visible damage to the dam or appurtenances | Potential |
|  | Earthquake resulting in uncontrolled release of water from the dam | Imminent |
| Security threat | Verified bomb threat that, if carried out, could result in damage to the dam. | Potential |
|  | Damage to dam or appurtenances with no impacts to the functioning of the dam | Potential |
|  | Detonated bomb that has resulted in damage to the dam or appurtenances | Imminent |
| Sabotage or vandalism | Damage to dam or appurtenance with no impacts to the functioning of the dam | Nonfailure |
|  | Modification to the dam or appurtenances that could adversely impact the functioning of the dam | Nonfailure |
|  | Damage to dam or appurtenances that has resulted in seepage flow | Potential |
|  | Damage to dam or appurtenances that has resulted in uncontrolled water release | Imminent |

* High Flow Emergency Level: Flooding of downstream people or infrastructure possible

* Nonfailure Emergency Level: Nonemergency unusual event, slowly developing

* Potential Failure Emergency Level: Potential dam failure situation, rapidly developing

* Imminent Failure Emergency Level: Urgent; dam failure is imminent or is in progress

#### Examples of Emergency Situations

The following are examples of conditions that usually constitute an emergency situation that may occur at a dam. Adverse or unusual conditions that can cause the failure of a dam are typically related to aging components, design and construction oversights, or extreme weather events that exceed designed conditions and can cause significant flow through the spillways or overtopping of the embankment. Accidental or intentional damage to the dam may also result in emergency conditions. The conditions have been grouped to identify the most likely emergency level condition. The groupings are provided as guidance only. Not all emergency conditions may be listed, and the dam operator is urged to use conservative judgment in determining whether a specific condition should be defined as an emergency situation at the dam.

Pre-existing conditions on this dam: There has been a small seepage area near the downstream toe on the north side of the release channel. This was first noticed in the 1990s, but has not changed since that time.

##### Earth or Structural Spillway Flows

High Flow Emergency Level—Flooding of downstream people or infrastructure possible:

1.   Flow through the spillways currently exceed or will likely exceed the safe downstream channel capacity that may cause flooding that could threaten people, homes, and/or roads downstream from the dam (not applicable to all dams). The depth of flow in the auxiliary spillway must be greater than shown in the Guidance Table on the previous page. Note that the flow depth is measured at the control section of the auxiliary spillway that is generally along centerline of the embankment.

##### Earth Spillway Flows

Potential Failure Emergency Level—Potential dam failure situation; rapidly developing:

1.	Significant erosion or head cutting of the earth spillway is in process, but the rate does not appear to threaten an imminent breach of the spillway crest that would result in an uncontrolled release of the reservoir.

Imminent Failure Emergency Level—Urgent; dam failure is imminent or is in progress:

- Significant erosion or head cutting of the earth spillway is occurring at a rapid rate, and a breach of the control section appears imminent

##### Embankment Overtopping

Potential Failure Emergency Level—Potential dam failure situation; rapidly developing:

- The reservoir level is less than 1 foot from the top of the dam.

- Water is flowing over the top of the dam, but no observed erosion.

Imminent Failure Emergency Level—Urgent; dam failure appears to be imminent or is in progress:

1.	Water is flowing over the embankment, with observed erosion of the embankment slope.

##### Seepage and Sinkholes

Potential Failure Emergency Level—Potential dam failure situation; rapidly developing:

1.	Observation of cloudy seepage or soil deposits at seepage exit points or from internal drain outlet pipes.

2.	Presence of new or increased areas of wet or muddy soils on the downstream slope, abutment, and/or foundation of the dam, with an easily detectable and unusual increase in volume of downstream seepage.

3.	Observation of one or more significant new or enlarging sinkholes near the dam or settlement of the dam.

4.	Reservoir level is falling without apparent cause.

5.	A rise in the reservoir will soon inundate the following known dam defects:

•	One or more sinkholes located on the upstream slope, crest, abutment, and/or foundation of the dam; or

•	Transverse cracks extending through the dam, abutments, or foundation.

Imminent Failure Emergency Level—Urgent; dam failure is imminent or is in progress:

1.	Rapidly increasing cloudy seepage or soil deposits at seepage exit points to the extent that failure appears imminent or is in progress.

2.	Rapid increase in volume of downstream seepage to the extent that failure appears imminent or is in progress.

3.	Water flowing out of holes in the downstream slope, abutment, and/or foundation of the dam to the extent that failure appears imminent or is in progress.

4.	Vortexes (whirlpools) or other evidence exists indicating that the reservoir is draining rapidly through the dam or foundation.

5.	One or more rapidly enlarging sinkholes are forming on the dam or abutments to the extent that failure appears imminent or is in progress.

6.	Rapidly increasing flow through one or more cracks eroding materials to the extent that failure appears imminent or is in progress.

##### Embankment Movement and Cracking

Potential Failure Emergency Level—Potential dam failure situation; rapidly developing:

1.	Settlement of the crest, slopes, abutments and/or foundation of the dam that may eventually result in breaching of the dam.

2.	Significant increase in length, width, or offset of cracks in the crest, slopes, abutments, and/or foundation of the dam that may eventually result in breaching of the dam.

Imminent Failure Emergency Level—Urgent; dam failure is imminent or is in progress:

1.	Sudden or rapidly moving slides, settlement, or cracking of the embankment crest, slopes, abutments, and/or foundation, and breaching of the dam appears imminent or is in progress.

Step 3	Notification and Communication

Notification

After the emergency level has been determined, the people on the following notification charts for the appropriate emergency level must be notified immediately. Communications are typically by phone; however, Twitter, Facebook, radio, email, or other means of communication may be used.

Communication

It is important to speak in clear and nontechnical terms to ensure those being notified understand what is happening, what the emergency level is, and what action to take.

Nonfailure Emergency Level—Unusual event; slowly developing

or

High Flow Emergency Level—Flooding of downstream people or infrastructure possible:

The conservation district manager and NRCS district conservationist should contact the NRCS State conservation engineer and State dam safety agency. A courtesy call to the county sheriff may be made to enhance situational awareness. Describe the situation including the estimated depth of flow and request technical assistance on next steps to take. If flooding of downstream people or property is imminent, notify entities on notification chart and explain that the dam is not failing but describe the specific properties that might be in danger.

Potential Failure Emergency Level—Potential dam failure situation; rapidly developing:

The following message should be used to help describe the emergency situation to the county sheriff .

“This is _____Identify yourself; name, position)_________.

We have an emergency condition at Rock Creek Watershed, Dam No. 23, located 2 miles south of Rock City. (Briefly describe situation). We have activated the emergency action plan for this dam and are currently under a Potential Failure Emergency Level.

We are implementing predetermined actions to respond to a rapidly developing situation that could result in dam failure. Please prepare to evacuate the area along low-lying portions of Rock Creek.

Reference the inundation map in your copy of the emergency action plan or an evacuation map if one was prepared.

We will advise you when the situation is resolved or if the situation gets worse.

I can be contacted at the following number: ___________________. If you cannot reach me, please call the following alternative number: ___________________.”

Imminent Failure Emergency Level—Urgent; dam failure is imminent or is in progress:

Immediately contact the county sheriff and evacuate the area (see Inundation Map tab). Take the following actions:

1.	Call the county sheriff’s dispatch center. Be sure to say, “This is an emergency.” They will call other authorities and the media and begin the evacuation. Use of the following message can help describe the emergency to the county sheriff:

“This is an emergency. This is _____Identify yourself; name, position)_________.

Rock Creek Watershed, Dam No. 23, located 2 miles south of Rock City, is failing. People in the downstream area must evacuate immediately. Repeat, Rock Creek Watershed, Dam No. 23, is failing; evacuate the area along low-lying portions of Rock Creek.

We have activated the emergency action plan for this dam and are currently under Imminent Failure Emergency Level. Reference the inundation map in your copy of the emergency action plan or an evacuation map if one was prepared.

You may contact me at the following number: ___________________. If you cannot reach me, please call the following alternative number: ___________________.”

2.	Do whatever is necessary to bring people in immediate danger (anyone on the dam, downstream from the dam, boating on the reservoir, or evacuees) to safety if directed by the sheriff.

3.	Keep in frequent contact with the sheriff and emergency services to keep them up-to-date on the condition of the dam. They will tell you how you can help handle the emergency.

4.	If all means of communication are lost: (1) try to find out why, (2) try to get to another radio or telephone that works, or (3) get someone else to try to re-establish communications. If these means fail, handle the immediate problems as well as you can, and periodically try to re-establish contact with the sheriff and emergency services.

Use the following prescripted message as a guide for the sheriff or Rock City emergency services personnel to communicate the status of the emergency with the public:

Attention:  This is an emergency message from the Rock City Emergency Management Director.  Listen carefully. Your life may depend on immediate action.

Rock Creek Watershed, Dam No. 23, located 2 miles south of Rock City, is failing. Repeat. Rock Creek Watershed, Dam No. 23, located 2 miles south of Rock City, is failing.

If you are in or near this area, proceed immediately to high ground away from the valley. Do not travel on Highway 44 south of Rock City or return to your home to recover your possessions. You cannot outrun or drive away from the flood wave. Proceed immediately to high ground away from the valley.

Repeat message.

Nonfailure Emergency Level Notifications

Unusual event; slowly developing

Potential Failure Emergency Level Notifications

Potential dam failure situation; rapidly developing

Note: this notification chart is also used for High Flow Emergency Level

Flooding of downstream people or infrastructure possible

Imminent Failure Emergency Level Notifications

Urgent event, dam failure is

imminent or is in progress

| Agency / Organization | Principal contact | Address | Primary telephone number | Alternate telephone numbers |
| --- | --- | --- | --- | --- |
| Coal County Board of Supervisors | Gloria Brown, Chair | 336 Highway 66 Rock City, OK | 407–555–XXXX | 407–555–XXXX |
| Coal County Road Department | Max Gray, Supervisor | 973 Ninth Street Rock City, OK | 407–555–XXXX | 407–555–XXXX |
| Coal County Conservation District | John Jordon District Manager | 523 Second Street Rock City, OK | 407–555–XXXX | 407–555–XXXX (H) 407–555–XXXX (C) |
| Coal County Conservation District | Mike Blain * Board Chair | 523 Second Street Rock City, OK | 407–555–XXXX | 407–555–XXXX (H) 407–555–XXXX (C) |
| Coal County Sheriff | Henry Martin | 336 Highway 66 Rock City, OK | 407–555–XXXX | 407–555–XXXX (H) 407–555–XXXX (C) |
| Dry Gulch Television Station KJMT | Chris Klinger Manager | 5632 Main Street Dry Gulch, OK | 407–555–XXXX | 407–555–XXXX |
| Landowner of Dam No. 23 | Bryon Babcock | R.R. #2 Rock City, OK |  | 407–555–XXXX (H) 407–555–XXXX (C) |
| National Weather Service | Danny Lee Climatologist | 66374 Elm Street Norman, OK | 618–555–XXXX | 407–555–XXXX |
| Natural Resources Conservation Service | Shelly Winters District Conservationist | 523 Second Street Rock City, OK | 407–555–XXXX | 407–555–XXXX (H) 407–555–XXXX (C) |
| Natural Resources Conservation Service | John Blake * Technician | 523 Second Street Rock City, OK | 407–555–XXXX | 407–555–XXXX (H) |
| Natural Resources Conservation Service | Robert Redford State Engineer | 3458 Farm Road Strong City, OK | 917–555–XXXX | 917–555–XXXX (H) 917–555–XXXX (C) |
| Natural Resources Conservation Service | John Jones Area Engineer | 523 Second Street Rock City, OK | 407–555–XXXX | 407–555–XXXX (H) 407–555–XXXX (C) |
| Oklahoma Department of Transportation | Bill Dobson District Engineer | 539 Center Street Dry Gulch, OK | 407–555–XXXX |  |
| Oklahoma Highway Patrol | Richard Barnell | 299 First Avenue Dry Gulch, OK | 407–555–XXXX |  |
| Oklahoma Water Resources Board | Joe Griswold Dam Safety Officer | 1522 Maple Avenue Strong City, OK | 618–555–XXXX | 618–555–XXXX (H) 618–555–XXXX (C) |
| Rock City Emergency Management Coordinator | Jeff Powers | 121 Main Street Rock City, OK | 407–555–XXXX |  |
| Rock City Fire Department | Harry James | 336 Maple Street Rock City, OK | 407–555–XXXX |  |
| Rock City Police | Red Jones | 336 Maple Street Rock City, OK | 407–555–XXXX |  |
| Rock City Radio Station 1040 AM | Scott Fagen Manager | 667 Eighth Street Rock City, OK | 407–555–XXXX |  |

Other Emergency Contacts

Step 4	Expected Actions

If the police or sheriff receives a 911 call regarding observations of an unusual or emergency event at the dam, they should immediately contact the conservation district office. After the conservation district manager determines the emergency level, and the initial notifications have been made, actions can many times be taken to minimize impacts to life and property. During this step, there is a continuous process of taking actions, accessing the status of the situation and keeping others informed through communication channels established during the initial notifications. The following are actions that should be taken for the situations shown. If time permits, contact NRCS and the State dam safety agency for technical consultation.

High Flow Emergency Level—Flooding of downstream people or infrastructure possible:

A. The conservation district manager should inspect the dam and estimate the depth of auxiliary spillway flow. If the flow depth is approaching the predetermined depth that may threaten downstream areas (see appendix B-6) and rain continues to fall, the conservation district manager should contact NRCS and request technical staff to recommend actions to take.

B. Record all contacts that were made on the Contact Checklist (appendix A–1). Record all information, observations, and actions taken on the Event Log Form (appendix A–2). Note the time of changing conditions. Document the situation with photographs and video, if possible.

Nonfailure Emergency Level—Unusual event; slowly developing:

A.	The conservation district manager should inspect the dam. At a minimum, inspect the full length of the upstream slope, crest, downstream toe, and downstream slope. Also, check the reservoir area, abutments, and downstream channel for signs of changing conditions. If increased seepage, erosion, cracking, or settlement are observed, immediately report the observed conditions to the NRCS or the State dam safety agency; refer to the emergency level table for guidance in determining the appropriate event level for the new condition and recommended actions.

B.	Record all contacts that were made, and all information, observations, and actions taken on the Event Log Form (appendix A–1). Note the time of changing conditions. Document the situation with photographs and video, if possible.

C.	The conservation district manager should contact NRCS and request technical staff to investigate the situation and recommend corrective actions.

Potential Failure Emergency Level—Potential dam failure situation; rapidly developing:

A.	The conservation district manager should contact the NRCS and the State dam safety agency to report the situation and, if time permits, request technical staff to investigate the situation and recommend corrective actions.

B.	The conservation district manager should contact county sheriff to inform him or her that the EAP has been activated and if current conditions get worse, an emergency situation may require evacuation. Preparations should be made for possible road closures and evacuations.

C.	Provide updates to the county sheriff to assist in making timely decisions concerning the need for warnings, road closures, and evacuations.

D.	If time permits, the conservation district manager should inspect the dam. At a minimum, inspect the full length of the upstream slope, crest, downstream toe, and downstream slope. Also, check the reservoir area, abutments, and downstream channel for signs of changing conditions. If piping, increased seepage, erosion, cracking, or settlement are observed, immediately report the observed conditions to the NRCS and the State dam safety agency; refer to the emergency level table for guidance in determining the appropriate event level for the new condition and recommended actions.

E.	Record all contacts that were made, and all information, observations, and actions taken on the Event Log Form (appendix A–1). Note the time of changing conditions. Document the situation with photographs and video, if possible.

F.	If time allows, the following emergency remedial actions should be taken as appropriate.

Emergency remedial actions

If time permits, the following emergency remedial actions should be considered by the Coal County Conservation District for Potential Failure Level Emergency conditions. Immediate implementation of these remedial actions may delay, moderate, or prevent the failure of the dam. Several of the listed adverse or unusual conditions may be apparent at the dam at the same time, requiring implementation of several modes of remedial actions. Close monitoring of the dam by experienced engineers must be maintained to confirm the success of any remedial action taken at the dam. Time permitting, any remedial action should be developed through consultation with NRCS and the State dam safety agency. See Resources Available (appendix B–1) for sources of equipment and materials to assist with remedial actions.

Embankment overtopping

1.	If the water level in the reservoir is no longer rising, place sandbags along the low areas of the top of the dam to control wave action, reduce the likelihood of flow concentration during minor overtopping, and to safely direct more water through the spillway.

2.	Cover the weak areas of the top of the dam and downstream slope with riprap, sandbags, plastic sheets, or other materials to provide erosion-resistant protection.

Seepage and sinkholes

1.	Open the principal spillway gate or low-level outlet works to lower the reservoir level as rapidly as possible to a level that stops or decreases the seepage to a non-erosive velocity. If the gate is damaged or blocked, pumping or siphoning may be required.

Continue lowering the water level until the seepage stops.

2.	If the entrance to the seepage origination point is observed in the reservoir (possible whirlpool) and is accessible, attempt to reduce the flow by plugging the entrance with readily available materials such as hay bales, bentonite, soil or rock fill, or plastic sheeting.

3.	Cover the seepage exit areas with several feet of sand/gravel to hold fine-grained embankment or foundation materials in place. Alternatively, construct sandbag or other types of ring dikes around seepage exit areas to retain a pool of water, providing backpressure and reducing the erosive nature of the seepage.

4.	Prevent vehicles and equipment from driving between the seepage exit points and the embankment to avoid potential loss from the collapse of an underground void.

Embankment movement

1.	Open outlets and lower the reservoir to a safe level at a rate commensurate with the urgency and severity of the condition of the slide or slump. If the gate is damaged or blocked, pumping or siphoning may be required.

2.	Repair settlement of the crest by placing sandbags or earth and rock fill materials in the damaged area to restore freeboard.

3.	Stabilize slides by placing a soil or rock fill buttress against the toe of the slide.

Earthquake

1.	Immediately conduct a general overall visual inspection of the dam.

2.	Perform a field survey to determine if there has been any settlement and movement of the dam embankment, spillway, and low-level outlet works.

3.	Drain the reservoir, if required.

Imminent Failure Emergency Level—Dam failure is imminent or is in progress:

A.	The conservation district manager must immediately contact the county sheriff and others shown on the notification chart.

B.	The county sheriff and emergency management personnel will lead the efforts to carry out warnings, close roads, and evacuate people at risk downstream from the dam (see Inundation Map tab).

C.	Emergency management services personnel must alert the public and immediately evacuate at-risk people and close roads, as necessary.

D.	The conservation district manager must maintain continuous communication and provide the sheriff with updates of the situation to assist him or her in making timely decisions concerning warnings and evacuations.

E.	The conservation district manager must record all contacts that were made, and all information, observations, and actions taken on the Event Log Form (appendix A–1). Note the time of changing conditions. Document the situation with photographs and video, if possible.

F.	Advise people monitoring the dam to follow safe procedures. Everyone should stay away from any of the failing structures or slopes and out of the potential breach inundation areas.

Step 5	Termination

Whenever the EAP has been activated, an emergency level has been declared, all EAP actions have been completed, and the emergency is over, the EAP operations must eventually be terminated and follow up procedures completed.

Termination responsibilities

Typically, the technical representative or state dam safety official will help determine when the condition of the dam has been stabilized. The incident commander is responsible for terminating EAP operations in consultation with qualified engineers and the dam owner. It is then the responsibility of each person to notify the same group of contacts that were notified during the original event notification process to inform those people that the event has been terminated. A final DamWatch ticket should be prepared and issued for future reference.

Prior to termination of any event that has not caused actual dam failure, the NRCS technical representative or the State dam safety officer will inspect the dam or require the inspection of the dam to determine whether any damage has occurred that could potentially result in loss of life, injury, or property damage. If the inspection determines that conditions do not pose a threat to people or property, the NRCS technical representative or the State dam safety officer will advise the conservation district manager and county sheriff  to terminate EAP operations as described above.

The conservation district manager must ensure completion of the Dam Emergency Situation Report (appendix A–2) to document the emergency event and all actions taken. The report should include an after-action review and evaluation that includes the following:

- Events or conditions leading up to, during, and following the incident

- Significant actions taken

- Strengths and deficiencies experienced in the incident management process, staffing, and leadership

- Corrective actions identified and a planned course of action to implement recommendations

The conservation district  must distribute copies of the completed report to the State dam safety agency and the NRCS State conservation engineer.

## Maintenance—EAP Review and Revision

EAP annual review

The conservation district manager  will review and, if needed, update the EAP at least once each year. The EAP annual review will include the following:

•	Calling all contacts on the notification charts in the EAP to verify that the phone numbers and people in the specified positions are current. Revise the EAP if any of the contacts have changed.

•	Contacting all plan holders to verify the phone numbers and people in the specified positions. In addition, the conservation district manager  will ask if the person contacted knows the location of the EAP and if the person understands responsibilities described in the EAP.

•	Calling the locally available resources to verify that the phone numbers, addresses, and services are current.

Revisions

The conservation district  is responsible for updating the EAP document. The EAP document held by the conservation district is the master document. When revisions occur, the conservation district  will provide the revised pages and a revised revision summary page to all the EAP document holders. The document holders are responsible for revising outdated copy of the respective documents whenever revisions are received. Outdated pages must be immediately discarded to avoid any confusion with the revisions.

EAP table top exercise

The conservation district  will host and facilitate a periodic test of the EAP at least once every 5 years.

The periodic test will consist of a meeting, including a tabletop exercise, conducted at the Coal County Conservation District office. Attendance should include the conservation district manager, key conservation district staff members, NRCS staff, at least one representative of the local law enforcement agency, and others with key responsibilities listed in the EAP. At the discretion of the conservation district  other organizations, such as the National Weather Service and others that may be involved with an unusual or emergency event at the dam are encouraged to participate. The tabletop exercise is an excellent time for developing interpersonal relationships with critical players of the team that will be involved when an emergency occurs. During the tabletop exercise, participants may visit the dam to familiarize themselves with the dam site and impacted downstream area.

The tabletop exercise will begin with the facilitator presenting a scenario of an unusual or emergency event at the dam. The scenario will be developed prior to the exercise. Once the scenario has been presented, the participants will discuss the responses and actions that they would take to address and resolve the scenario. The narrator will control the discussion, ensuring realistic responses and developing the scenario throughout the exercise. The conservation district manager should complete an event log as they would during an actual event. The simulator tool and documents in DamWatch may be used to assist with providing a real-world example situation.

After the tabletop exercise, review and discuss the five sections of the EAP. Discuss mutual aid agreements and other emergency procedures and actions. Discussions and actions discussed could include the addition of helpful appurtenances, such as remote cameras or a staff gauge in the reservoir to indicate water level, or the purchase of portable lighting equipment. The conservation district  will prepare a written summary of the tabletop exercise and revise or update the EAP, as necessary.

## Record of Holders of Control Copies of this EAP

The holders of the official copies of the EAP should add their initials and date next to their name shown below when they receive their copy of this EAP. Their initials signify that they have reviewed the EAP and that they concur with the tasks and responsibilities assigned to them and their organization. The Coal County Conservation District should retain the initialized copy.

| Copy Number | Organization | Person receiving copy |
| --- | --- | --- |
| 1 | Coal County Conservation District 523 Second Street Rock City, OK 50010 | John Jordan District Manager, Coal Co.Coal Co. Cons. District |
| 2 | NRCS Field Office 523 Second Street Rock City, OK 50010 | Shelly Winters NRCS District Conservationist |
| 3 | NRCS State Office 3458 Farm Road Strong City, OK 51020 | Robert Redford NRCS State Conservation Engineer |
| 4 | Coal County Sheriff’s Department 336 Highway 66 Rock City, OK 50010 | Henry Martin Coal County Sheriff |
| 5 | Rock City Emergency Management 121 Main Street Rock City, OK 50010 | Jeff Powers Rock City Emergency Manager |
| 6 | Rock City Police Department 336 Maple Street Rock City, OK 50010 | Red Jones Police Chief, Rock City, OK 50010 |
| 7 | State Dam Safety Agency Division of Water Resources 1320 Research Park Drive Manhattan KS 66502 | Terry Medley Water Structures Program Manager |

## Record of Revisions and Updates Made to EAP

| Revision Number | Date | Revisions made | By whom |
| --- | --- | --- | --- |
| 1 | 4-25-17 | Updated EAP with current contact information for Conservation District personnel and names of new residents in evacuation area | John Jordon |

## Appendices—Forms, Glossary, Maps, and 
Supporting Data

Appendix A

A–1	Unusual or Emergency Event Log Form

A–2	Dam Emergency Situation Report Form

A–3	Glossary of Terms

A-4    Contact Checklist

Appendix B

B–1	Resources Available

B–2	Location and Vicinity Maps

B–3	Watershed Project Map

B–4	Inundation Maps

B–5	Residents/Businesses/Highways at Risk

B–6	Residents/Businesses/Highways at Risk for High Auxiliary Spillway Flow

B–7	Plan View of Dam

B–8	Profile of Principal Spillway

B–9	Reservoir Elevation-Area-Volume and Spillway Capacity Data

B–10	National Inventory of Dams (NID) Data

## Appendix A–1

#### Unusual or Emergency Event Log

(to be completed during the emergency)

Dam name:     Rock Creek Watershed, Dam No. 23                          County:       Coal County

When and how was the event detected? _____________________________________________________________________________

_____________________________________________________________________________

Weather conditions: _____________________________________________________________

_____________________________________________________________________________

General description of the emergency situation: _____________________________________________________________________________

_____________________________________________________________________________

_____________________________________________________________________________

Emergency level determination: ______________  Made by: ____________________________

#### Actions and Event Progression

#### Include notes of all people contacted, the person making the contacts, and the time of the contact.

#### See the Notification Charts and Emer. Services Contacts tabs for critical contact information.

| Date | Time | Action/event progression | Taken by |
| --- | --- | --- | --- |

Report prepared by: _______________________________________  Date: _______________

## Appendix A–2

#### Dam Emergency Situation Report

(to be completed following the termination of the emergency)

Dam name:  Rock Creek Watershed, Dam No. 23

National Inventory of Dams (NID) No.: OK11111

Dam location:  2 miles south of Rock City                    Coal County          Rock Creek

(City)                                              (County)                (Stream/River)

Event initiated: Date:          Time:         Event terminated: Date:          Time:

Weather conditions: ____________________________________________________________

General description of emergency situation: _____________________________________________________________________________

_____________________________________________________________________________

Areas of dam affected: _____________________________________________________________________________

_____________________________________________________________________________

Extent of dam damage:  _________________________________________________________

Possible causes: ______________________________________________________________

Effect on dam’s operation:_______________________________________________________

Initial reservoir elevation: _______________________	Time: ______________

Maximum reservoir elevation: ______________________	Time: ______________

Final reservoir elevation: _________________________	Time: ______________

Description of area flooded downstream/damages/injuries/loss of life: ____________________

______________________________________________________________________________

Other data and comments: ______________________________________________________________________________

Observer’s name and telephone number:_________________________________________

Report prepared by: ________________________________________    Date: ______________

## Appendix A–3
Glossary of Terms

Abutment	That part of the valley side against which the dam is constructed. The left and right abutments of dams are defined with the observer looking downstream from the dam.

Acre-foot	A unit of volumetric measure that would cover 1 acre to a depth of 1 foot. One acre-foot is equal to 43,560 cubic feet or 325,850 gallons.

Berm	A nearly horizontal step (bench) in the upstream or downstream sloping face of the dam.

Boil	A disruption of the soil surface due to water discharging from below the surface. Eroded soil may be deposited in the form of a ring (miniature volcano) around the disruption.

Breach	An opening through the dam that allows draining of the reservoir. A controlled breach is an intentionally constructed opening. An uncontrolled breach is an unintended failure of the dam.

Conduit	A closed channel (round pipe or rectangular box) that conveys water through, around, or under the dam.

Control section	A usually level segment in the profile of an open channel spillway above which water in the reservoir discharges through the spillway.

Cross section	A slice through the dam showing elevation vertically and direction of natural water flow horizontally from left to right. Also, a slice through a spillway showing elevation vertically and left and right sides of the spillway looking downstream.

Dam	An artificial barrier generally constructed across a watercourse for the purpose of impounding or diverting water.

Dam failure	The uncontrolled release of a dam’s impounded water.

Dam operator	The people or units of government with responsibility for the operation and maintenance of dam.

DamWatch®		A web-based application developed by USEngineering Solutions Corporation to assist dam owners to monitor and manage NRCS-assisted dams. It provides real-time monitoring of meteorological events and alerts essential personnel by email or text when dams experience potentially hazardous conditions. It also stores critical information, such as EAPs, inspection reports, and as-built drawings.

Drain (toe or foundation)	A water collection system of sand and gravel and possibly pipes along the downstream portion of the dam to collect seepage and convey it to a safe outlet.

Drainage area (watershed)	The geographic area on which rainfall runoff flows into the dam

Drawdown 	The lowering or releasing of the water level in a reservoir over time or the volume lowered or released over a particular period of time.

Emergency	A condition that develops unexpectedly, endangers the structural integrity of the dam and/or downstream human life and property, and requires immediate action to protect life and property.

Emergency action plan	A formal document identifying potential emergency conditions that may

(EAP) 	occur at the dam and specifying preplanned actions to minimize potential failure of the dam or minimize failure consequences including loss of life, property damage, and environmental impacts.

Filter	The layers of sand and gravel in a drain that allow seepage through an embankment to discharge into the drain without eroding the embankment soil.

Freeboard	Vertical distance between a stated water level in the reservoir and the top of dam.

Gate, slide or sluice, 	An operable, watertight valve to manage the discharge of water from the

or regulating 	dam.

Groin	The area along the intersection of the face of a dam and the abutment.

Hazard potential	A system that categorizes dams (high, significant, or low) according to

classification 	the classification degree of their potential to create adverse incremental consequences such as loss of life, property damage, or environmental impacts of a failure or misoperation of a dam.

Height, dam	The vertical distance between the lowest point along the top of the dam and the lowest point at the downstream toe, which usually occurs in the bed of the outlet channel.

Hydrograph, inflow or 	A graphical representation of either the flow rate or flow depth at a

outflow, or breach  specific point above or below the dam over time for a specific flood occurrence.

Incident commander	The highest predetermined official available at the scene of an emergency situation.

Instrumentation	An arrangement of devices installed into or near dams that provide measurements to evaluate the structural behavior and other performance parameters of the dam and appurtenant structures.

Inundation area or map	The geographic area downstream of the dam that could be flooded by a breach of the dam or other large discharge.

Notification	To immediately inform appropriate individuals, organizations, or agencies about a potentially emergency situation so they can initiate appropriate actions.

Outlet works	An appurtenant structure that provides for controlled passage of normal

(principal spillway)	water flows through the dam.

Periodic test	An exercise that involves all people with key responsibilities identified in the emergency action plan to review the emergency action plan discuss the tasks and responsibilities in the response to a simulated event

Piping	The progressive destruction of an embankment or embankment foundation by internal erosion of the soil by seepage flows.

Probable maximum 	The theoretically greatest precipitation or resulting flood that is

precipitation (PMP) or 	meteorologically feasible for a given duration over a specific drainage area

flood (PMF) 	at a particular geographical location.

Reservoir	The body of water impounded or potentially impounded by the dam.

Riprap	A layer of large rock, precast blocks, bags of cement, or other suitable material, generally placed on an embankment or along a watercourse as protection against wave action, erosion, or scour.

Risk	A measure of the likelihood and severity of an adverse consequence.

Seepage	The natural movement of water through the embankment, foundation, or abutments of the dam.

Slide	The movement of a mass of earth down a slope on the embankment or abutment of the dam.

Spillway (auxiliary 	The appurtenant structure that provides the controlled conveyance of

or emergency) 	excess water through, over, or around the dam.

Spillway capacity	The maximum discharge the spillway can safely convey with the reservoir at the maximum design elevation.

Spillway crest	The lowest level at which reservoir water can flow into the spillway.

Tailwater	The body of water immediately downstream of the embankment at a specific point in time.

Toe of dam	The junction of the upstream or downstream face of an embankment with the ground surface.

Top of dam (crest of dam)	The elevation of the uppermost surface of an embankment that can safely impound water behind the dam.

## Appendix A–4

### Contact Checklist

Rock Creek Watershed, Dam No. 23

Coal County, Oklahoma	Date _____________

The following contacts should be made immediately after the emergency level is determined (see pages 
7–10 for guidance to determine the appropriate emergency level for a specific situation). The person making the contacts should initial and record the time of the call and who was notified for each contact made. See the Notification Charts tab for critical contact information and Emer. Services Contacts tab for contact information for other possible emergency services.

Emergency Level 1 (see page 12)	Person	Time	Contacted

Contacted	Contacted	by

___ NRCS District Conservationist	_____________	_____________	_____________

___ NRCS State Conservation Engineer	_____________	_____________	_____________

___ Division of Water Resources	_____________	_____________	_____________

Emergency Level 2 (see page 13)	Person	Time	Contacted

Contacted	Contacted	by

____ NRCS District Conservationist  	_____________	_____________	_____________

____ NRCS State Conservation Engineer 	_____________	_____________	_____________

____ Division of Water Resources	_____________	_____________	_____________

____ Sheriff	_____________	_____________	_____________

Emergency Level 3 (see page 14)	Person  	Time	Contacted

Contacted	Contacted	by

____ Sheriff	_____________	_____________	_____________

____ Division of Water Resources	_____________	_____________	_____________

____ NRCS District Conservationist 	_____________	_____________	_____________

____ NRCS State Conservation Engineer	_____________	_____________	_____________

## Appendix B–1
Resources Available

Locally available equipment, labor, and materials:

The County Commissioners have the following resources that can be utilized in the event of an emergency:

•	two front-end loaders

•	two backhoes

•	one track hoe

•	two graders

•	two dump trucks

•	a sand borrow pit

•	a clay borrow pit

Contact the Coal County Road Department—see Emer. Services Contacts tab.

Other locally available resources include:

| Heavy equipment service and rental | Sand and gravel supply | Ready-mix concrete supply |
| --- | --- | --- |
| Bob’s Dozer Service 134 Elm Street Rock City, OK 407–555–XXXX | Kern’s Sand and Gravel R.R. 2 Rock City, OK 407–555–XXXX | Burnett Concrete Co. 231 Sixth Street Dry Gulch, OK 407–555–XXXX |
| Tiller Construction Co. 405 Second Street Dry Gulch, OK 407–555–XXXX | Renfro Sand Products 334 Aston Avenue Spring Lake, OK 407–555–XXXX |  |
| Pumps | Diving contractor | Sand bags |
| A to Z Rental 569 Seventh Street Rock City, OK 407–555–XXXX | Steve White 2201 56th Street Johnstown, OK 917–555–XXXX | A to Z Rental 5643 Water Street Johnstown, OK 917–555–XXXX |

## Appendix B–2
Location and Vicinity Maps

(Insert map)

## Appendix B–3
Watershed Project Map

(Insert map)

## Appendix B–4
Inundation Map

(Insert map)

## Appendix B–5
Residents/Businesses/Highways at Risk

A major flood caused by a sudden breach of the dam is estimated to inundate six homes, three businesses, and three highways. These homes and businesses (marked on the inundation map) are located east of OK Highway 44 and south of Chestnut Street in Rock City.

| House/ business no.* | Resident/business | Address | Phone no. | Distance downstream from dam (ft.) | Travel time** (hr.) | Max water depth above first floor (ft.) |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Fred and Ethel James | 10300 132nd Street | 555–XXXX | 5,000 | 0.3 | 5.4 |
| B-2 | Larry’s Hardware | 3214 Chestnut Street | 555–XXXX | 11,400 | 0.9 | 0.8 |
| B-3 | Lori’s Music Shop | 2288 Farm Road | 555–XXXX | 11,600 | 0.9 | 2.6 |
| B-4 | Bill’s Coffee Shop | 1455 Sugar Street | 555–XXXX | 11,800 | 1.0 | 4.8 |
| 5 | Terry and Ann Smith | 4812 Chestnut Street | 555–XXXX | 13,600 | 1.1 | 3.0 |
| 6 | Amos Hill | 5500 Apple Road | 555–XXXX | 14,000 | 1.1 | 3.2 |
| 7 | Allen and Ruth Jones | 4814 Chestnut Street | 555–XXXX | 13,800 | 1.1 | 1.2 |
| 8 | Mike and Carol Green | 4902 Chestnut Street | 555–XXXX | 14,000 | 1.1 | 2.4 |
| 9 | Stephanie Evans | 4910 Chestnut Street | 555–XXXX | 14,200 | 1.1 | 0.5 |
|  | OK Highway 44 |  |  | 2,000 | 0.2 | 7.9 |
|  | Interstate 40 |  |  | 10,000 | 0.8 | 3.4 |
|  | OK Route 66 |  |  | 11,200 | 0.9 | 3.4 |

* See appendix B–4.

** Estimated time for breach wave (peak) to travel from dam to downstream locations

Basis for computation of inundation area and flooding depths

Breach inundation study completed by NRCS–August 2016

Hydraulic model used: NRCS TR–20 (routing); TR–60 (peak discharge); TR–66 (hydrograph)

Model assumptions:

	“Sunny Day” Breach (no inflow into the reservoir)

	Water surface elevation in reservoir prior to breach = _______ (top of dam)

	Total volume of breach hydrograph = ______ acre-ft.

	Height of water at time of breach = ______ ft.

	Peak breach discharge = _______ ft3/s

	Downstream area defined by LiDAR imagery dated 3-18-15 and field surveys of 3 bridge openings

## Appendix B–6

## High Flow Emergency Level

## Residents/Businesses/Highways at Risk

If the auxiliary spillway flows at depths shown below, the following infrastructure may be inundated:

| House/ business no.* | Resident/ business | Address | Phone no. | Aux. Spillway Flow depth (ft.) | Capacity (cfs) |
| --- | --- | --- | --- | --- | --- |
| 1 | Fred and Ethel James | 10300 132nd Street | 555–XXXX | 1.5 | 1,800 |
| B-4 | Bill’s Coffee Shop | 1455 Sugar Street | 555–XXXX | 2.0 | 2,300 |
|  | OK Highway 44 |  |  | 1.0 | 1,000 |

* See appendix B–4

## Appendix B–7
Plan View of Dam

(Insert Drawing)

## Appendix B–8
Profile of Principal Spillway

(Insert Drawing

## Appendix B–9
Reservoir Elevation-Area-Volume 
and Spillway Capacity Data

ROCK CREEK WATERSHED 
DAM NO. 23

| Elevation | Reservoir Surface acres | Reservoir Storage acre ft | Spillway Discharge ft3/s |
| --- | --- | --- | --- |
| 1682.0 | 0.0 | 0.0 | 0 |
| 1684.0 | 0.3 | 0.3 | 0 |
| 1686.0 | 2.0 | 2.5 | 0 |
| 1688.0 | 3.7 | 8.2 | 0 |
| 1690.0 | 8.6 | 20.5 | 0 |
| 1692.0 | 15.9 | 45.0 | 0 |
| 1694.0 | 18.7 | 79.6 | 9 |
| 1696.0 | 23.5 | 121.8 | 0 |
| Principal Spillway Crest |
| 1697.0 | 26.2 | 146.7 | 0 |
| 1698.0 | 31.1 | 175.4 | 45 |
| 1700.0 | 40.8 | 247.3 | 76 |
| 1702.0 | 49.3 | 337.4 | 82 |
| 1704.0 | 62.0 | 448.7 | 87 |
| 1706.0 | 71.4 | 582.1 | 92 |
| 1708.0 | 86.7 | 740.2 | 97 |
| 1710.0 | 98.6 | 925.5 | 102 |
| Auxiliary Spillway Crest |
| 1712.0 | 115.0 | 1139.1 | 108 |
| 1714.0 | 129.9 | 1384.0 | 516 |
| 1716.0 | 145.3 | 1659.2 | 2090 |
| 1718.0 | 160.7 | 1965.2 | 4437 |
| 1720.0 | 178.8 | 2304.7 | 7763 |
| 1720.2 | 180.6 | 2340.6 | 7937 |

## Appendix B–10
National Inventory of Dams (NID) Data

Dam name: ________

State: ________

NID ID: ________

Longitude:– ________

Latitude: ________

Geodetic location: ________

County: ________

Stream: ________

Nearest town: ________

Distance to nearest town: ___ mi.

Operator: ________ Cons. District

Year constructed: ________

Year rehabilitated: ________

Dam height: ____ ft.

Dam length: _____ ft.

Dam volume: _____ yd3

Max. discharge: ____ ft3/s

Max. storage: _____acre-ft.

Normal storage: _____ acre-ft.

Surface area: ___ acre

Drainage area: ___ mi2

Inspection frequency: 1 yr.

State regulated?: Yes

State reg. agency: ________

Federal funding: USDA NRCS

Federal design: USDA NRCS

Federal constructed: USDA NRCS

Program authority: Flood prevention

Watershed No.: _____

Watershed name: ________

Service life: ___ yr.

O&M insp. resp.: ________ Cons. District

O&M insp. current?: _____

Population at risk: __

Design hazard potential classification: ____

Current hazard potential classification: _____

Hazard potential classification year: ____

Sediment storage: ____ acre-ft.

Flood storage: _____ acre-ft.

Surcharge storage: ____ acre-ft.

Other storage: ____ acre-ft.

Principal spillway type: Concrete pipe

Principal spillway conduit diameter: ___ in.

Auxiliary spillway type: Vegetated earth

Auxiliary spillway width: _____ ft.

# Text boxes

Insert state map showing location of dam

Insert local area map showing specific location of dam

Dam Operator’s Representative

Coal County Conservation District Manager

John Jordan

407–555–XXXX (Office)

407–555–XXXX (Home)

407–555–XXXX (Cell)

See Emer. Services Contacts tab for contact

information for backups to the people shown above

and other emergency personnel.

Note:

1, 2, etc., denotes call sequence

Legend:

Calls by operator 	 ______

Second level calls - - - - -

NRCS State Engineer

Robert Redford

917–555–XXXX (Office)

917–555–XXXX (Home)

917–555–XXXX (Cell)

Dam Operator’s

Technical Representative

NRCS District Conservationist

Shelly Winters

407–555–XXXX (Office)

407–555–XXXX (Home)

407–555–XXXX (Cell)

State Dam Safety

Official

Division of Water Resources

Terry Medley

(785) 564-6700 (Office)

1-(800) 915-6163 (Emergency After Hours)

(1)

(2)

Incident Commander

Sheriff

Henry Martin

407–555–XXXX (Office)

407–555–XXXX (Home)

See Emer. Services Contacts tab for contact information for backups to the people shown above and other emergency personnel.

Rock City Police

Dispatcher

National Weather Service

618–555–XXXX

Coal County Amateur

Radio Association:

John Turney

KE5GBD

407–555–XXXX

See Communications tab for prescripted messages.

Note:

1, 2, etc., denotes call sequence

Legend:

Calls by operator  _______

Second level calls - - - - - -

State Dam Safety

Official

Division of Water Resources

Terry Medley

(785) 564-6700 (Office)

1-(800) 915-6163 (Emergency After Hours)

Dam Operator’s

Technical Representative

NRCS District Conservationist

Shelly Winters

407–555–XXXX (Office)

407–555–XXXX (Home)

407–555–XXXX (Cell)

OK Highway Patrol

Dispatcher

(3)

(2)

(1)

Dam Operator’s Representative

Coal County Conservation District Manager

John Jordan

407-555-XXXX (Office)

407-555-XXXX (Home)

407-555-XXXX (Cell)

Rock City Emergency

Management

Dispatcher

NRCS State Engineer

Robert Redford

917–555–XXXX (Office)

917–555–XXXX (Home)

917–555–XXXX (Cell)

Incident Commander

Sheriff

Henry Martin

407–555–XXXX (Office)

407–555–XXXX (Home)

407–555–XXXX (Cell)

or

24-Hour 911

OK Highway Patrol

Dispatcher

Rock City Emergency

Management

Dispatcher

See Emer. Services Contacts tab for contact information for backups to the people shown above and other emergency personnel.

NRCS State Engineer

Robert Redford

917–555–XXXX (Office)

917–555–XXXX (Home)

917–555–XXXX (Cell)

Note:

1, 2, etc., denotes call sequence

Legend

Calls by operator _______

Second level calls - - - - -

See Communications tab

for prescripted messages.

Dam Operator’s

Technical Representative

NRCS District Conservationist

Shelly Winters

407–555–XXXX (Office)

407–555–XXXX (Home)

407–555–XXXX (Cell)

State Dam Safety

Official

Division of Water Resources

Terry Medley

(785) 564-6700 (Office)

1-(800) 915-6163 (Emergency After Hours)

Coal County Amateur

Radio Association:

John Turney

KE5GBD

407–555–XXXX

National Weather Service

618–555–XXXX

(3)

(2)

(1)

Dam Operator’s Representative

Coal County Conservation District Manager

John Jordan

407–555–XXXX (Office)

407–555–XXXX (Home)

407–555–XXXX (Cell)

Rock City Police

Dispatcher